Radiation Protection Dosimetry 2004 110(1-4):693-698; doi:10.1093/rpd/nch176

Radiation Protection Dosimetry Vol. 110 Nos. 1-4 © Oxford University Press 2004; all rights reserved

## Neutron fluence-to-dose conversion coefficients for embryo and fetus

Jing Chen*, Dorothy Meyerhof and Slavica Vlahovich

Radiation Protection Bureau, Health Canada 6302D1, 775 Brookfield Road, Ottawa K1A 1C1, Canada

* Corresponding author: jing_chen@hc-sc.gc.ca

A problem of concern in radiation protection is the exposure of pregnant women to ionising radiation, because of the high radiosensitivity of the embryo and fetus. External neutron exposure is of concern when pregnant women travel by aeroplane. Dose assessments for neutrons frequently rely on fluence-to-dose conversion coefficients. While neutron fluence-to-dose conversion coefficients for adults are recommended in International Commission on Radiological Protection publications and International Commission on Radiological Units and Measurements reports, conversion coefficients for embryos and fetuses are not given in the publications. This study undertakes Monte Carlo calculations to determine the mean absorbed doses to the embryo and fetus when the mother is exposed to neutron fields. A new set of mathematical models for the embryo and fetus has been developed at Health Canada and is used together with mathematical phantoms of a pregnant female developed at Oak Ridge National Laboratory. Monoenergetic neutrons from 1 eV to 10 MeV are considered in this study. The irradiation geometries include antero-posterior (AP), postero-anterior (PA), lateral (LAT), rotational (ROT) and isotropic (ISO) geometries. At each of these standard irradiation geometries, absorbed doses to the fetal brain and body are calculated; for the embryo at 8 weeks and the fetus at 3, 6 or 9 months. Neutron fluence-to-absorbed dose conversion coefficients are derived for the four age groups. Neutron fluence-to-equivalent dose conversion coefficients are given for the AP irradiations which yield the highest radiation dose to the fetal body in the neutron energy range considered here. The results indicate that for neutrons <10 MeV more protection should be given to pregnant women in the first trimester due to the higher absorbed dose per unit neutron fluence to the fetus.

Radiation Protection Dosimetry 2006 118(4):378-383; doi:10.1093/rpd/nci378

Published by Oxford University Press (2006).

## Fluence-to-absorbed dose conversion coefficients for use in radiological protection of embryo and foetus against external exposure to protons from 100 MeV to 100 GeV

Jing Chen*

Radiation Protection Bureau, Health Canada, 775 Brookfield Road, Ottawa, Canada K1A 1C1

* Corresponding author: jing_chen@hc-sc.gc.ca

Received August 10, 2005, amended November 11, 2005, accepted December 5, 2005

In the literature, no conversion coefficients are available for use in radiological protection of embryo and foetus against external exposure to protons. This study used the Monte Carlo code MCNPX to determine mean absorbed doses to the embryo and foetus when the mother is exposed to proton fields. Monoenergetic protons ranging from 100 MeV to 100 GeV were considered. The irradiation geometries include antero–posterior (AP), postero–anterior (PA), lateral (LAT), rotational (ROT) and isotropic (ISO). At each of these standard irradiation geometries, absorbed doses to the foetal brain and body were calculated for the embryo of 8 weeks and the foetus of 3, 6 or 9 months. Proton fluence-to-absorbed dose conversion coefficients were derived for the four prenatal ages.